# Lecture 26 California Design Method

Traffic

Uses the ESAL and a formula to calculate a traffic index, TI

# Material

Sub base is defined using a stability meter value R. The value is determined using the California Stabilometer or Hveen Test.

# Environment

Environment is not directly considered in the procedure although the fact that it is for California sets the environment somewhat.

# The equation for the solution is

Where the Ge value is gravel equivalents and is in feet. Gavel equivalents for various materials are given in Table 20.19 reproduced below

The gravel equivalents are reduced to layer thickness in the same manner as the AASHTO method except the Ge of each of the layer are successively substituted to obtain the layer thickness

# The metric (mm) version is

Sample calculation follows

Given

ESAL=5x106

Mr sub grade = 5000 psi = 1000+555R

Rsub grade = 7.2

Mr sub base = 10000 psi = 1000+555R

Rsub base = 16.2

Mr base = 20000 psi = 1000+555

Rbase = 34.2

Calculations

See Chap 6 from the Federal Lands Highways Design Manual for additional information on soils and pavement design matters