CE  3401

Volume Calculations

Lecture 33-Lab 6

The total earthwork volume to be excavated/placed is an important figure to know.  This figure can indicate how cost-effective a project will be.  The volume will be calculated using the average end areas calculated in last week’s lab.  A spreadsheet would be ideal for you to calculate the volume.

The spreadsheet should be set up to include the following:

Cut Area: Referring to your cross-sections, record the calculated “cut” areas.

Fill Area: Referring to your cross-sections, record the calculated “fill” areas.

Adjusted Fill Area Multiply the Fill area by 10% for shrinkage

Cut Volume:Use the average end area volume formula.  Treat as +

Fill Volume: Use the average end area volume formula .  Treat as -

where	V	=	volume in cubic yards

A1	=	area of first station in square feet

A2	=	area of second station in square feet

L	=	length between stations A1 and A2 in feet

Net Volume is the accumulated sum of cut - fill.

As a final check, the sum of the Cut Vol – Fill Vol = Net Vol for your last station.  It should look something like this.

This lab assignment is due in lab next week.   You should submit the spreadsheet showing your calculations and a mass diagram comparable to the one shown above.