Lecture 43 Highway Capacity and Closure

Capacity is defined as the maximum number of passenger cars that can transverse a point under prevailing conditions.  It is a method of estimating the operational conditions on a roadway.  Because the relationship between speed and volume for a road doesn’t provide a unique solution the concept of level of service is introduced.  There are six level of service from A to F. Each is a progressively more congested flow.  LOS A is Free flow and LOS F is forced flow with frequent stop and go driving conditions.  The AASHTO Guide gives a description of each LOS.

LOS is used in both design and analysis of highway flow conditions.

For design the required LOS is a function of terrain and functional classification of the road.

Level of Service for a freeway is related to the prevailing conditions and is determined from the equation

In this equation the subscript represents the actual level of service and

MSF = Maximum Service Flow for LOS I Table 6.3

SF = the service flow = volume/PHF

PHF = peak Hour factor

N = Number of lanes

fw = correction for lane width and side clearance Table 6.4

fhv = correction for heavy vehicles Table 6.5

fp = correction for driver experience 0.75 to 1.0

Shock Wave

Disturbances on a roadway can cause traffic flow to vary from on e condition to another.  This can be illustrated by using shock wave analysis as presented in various transportation text.